## Slide 1: Unit 6 managing aviation services

## Slide 2: Learning outcome 3
Assess the different operational requirements of passenger service operations and airside operations

## Slide 3: p5
Compare and contrast the different service operations in terminal and airside to meet with regulations and operational standards

## Slide 4: A Day in the Life of an Airside Operations Officer

## Slide 5: maximum payload utilisation and Zero Fuel Weight(ZFW) calculations
Maximum payload capacity means the maximum certificated takeoff weight of an aircraft less the empty weight, less all justifiable aircraft equipment, and less the operating load (consisting of minimum fuel load, oil, flight crew, steward's supplies, etc.).
Empty weight is defined as the weight of the airframe, engines, propellers, and fixed equipment of an aircraft. Empty weight excludes the weight of the crew and payload, but includes the weight of all fixed ballast, unusable fuel supply, undrainable oil, total quantity of engine coolant, and total quantity of hydraulic fluid.
The maximum allowable weight for an aircraft is determined by design considerations. The manufacturer provides the aircraft operator with the empty weight of the aircraft and the location of its empty weight center of gravity (EWCG) at the time the certified aircraft leaves the factory.

## Slide 6: maximum payload utilisation and Zero Fuel Weight (ZFW) calculations
For purposes of this part, the allowance for weight of the crew, oil and fuel is as follows:
Crew - 200 pounds per crew member required under FAA regulations,
oil - 350 pounds
fuel - the minimum weight of fuel required under FAA regulations for a flight between domestic points 200 miles apart, assuming VFR weather conditions and flights not involving extended overwater operations. However, in the case of aircraft for which a maximum zero fuel weight is prescribed by the FAA, maximum payload capacity means the maximum zero fuel weight less the empty weight, less all justifiable aircraft equipment, and less the operating load (consisting of minimum flight crew, steward's supplies, etc., but not including disposable fuel or oil).

## Slide 7: maximum payload utilisation and Zero Fuel Weight (ZFW) calculations
Small aircraft means any aircraft designed to have:
A maximum passenger capacity of not more than 30 seats and a maximum payload capacity of not more than 7,500 pounds, and/or
maximum authorized takeoff weight on wheels not greater than 35,000 pounds

## Slide 8: maximum payload utilisation and Zero Fuel Weight (ZFW) calculations
The maximum design zero-fuel weight is the maximum certificated design weight of the aircraft less all usable fuel and other specified usable agents as limited by aircraft strength and airworthiness requirements.
It is the maximum weight permitted before usable fuel and other specified usable fluids are loaded in specified sections of the airplane.
The weight difference between the maximum design takeoff weight (MDTOW) and the maximum design zero-fuel weight (MDZFW) may be utilized only for the addition of fuel.
MAXIMUM PAYLOAD = MDZFW - OEW

## Slide 9: maximum payload utilisation and Zero Fuel Weight (ZFW) calculations
Let’s start with the aircraft itself. An aircraft “as is” includes:
Airframe structure with all moving mechanical parts (fuselage, wings, flaps, gear, rudder, nacelle …)
Power generation system (APU, main engines, power plant…)
Systems (electrical, hydraulics, pneumatic, fuel flow system, instrument, navigation, air conditioning, anti-ice, fixed furnishing)
Fixed equipment and services considered an integral part of the aircraft
Fixed ballast
Closed system fluids
Unused fuel only for small aircraft
All these items above form the Manufacturer’s Empty Weight (MEW)

## Slide 10: maximum payload utilisation and Zero Fuel Weight (ZFW) calculations
This weight does not include:
Fuel
Oil, potable water
Payload (Cargo, passenger, luggage)
Removable equipment
Customer specific installations or operator items

## Slide 11: maximum payload utilisation and Zero Fuel Weight (ZFW) calculations
Manufacturer’s Empty weight (MEW) + Operators Item = Operational Empty Weight (OEW)
The operator’s items are:
fluids necessary for aircraft operation (engine oil and coolant, water, unusable fuel)
the water for galleys and lavatories
aircraft documentation
passenger seats (and the life vests)
galley structure
catering emergency equipment
aircraft crew and their luggage.
standard items necessary for full operation

## Slide 12: maximum payload utilisation and Zero Fuel Weight (ZFW) calculations
The MEW and the operator’s items are summed up to the Operational Empty Weight (OEW). The OEW is usually fixed for a specific aircraft and only gets changed during maintenance or operational changes.
Operational Empty Weight (OEW) is the empty weight that is used in the flight simulator or the usual planning software

## Slide 13: maximum payload utilisation and Zero Fuel Weight (ZFW) calculations
Operational Empty Weight (OEW) + Payload = Actual Zero Fuel Weight (AZFW)
The payload includes:
the passengers weight (the standard weights used defined by ICAO respectively)
the passengers luggage’s weight
the cargo weight
Cargo + Passengers & Luggage = Payload

## Slide 14: maximum payload utilisation and Zero Fuel Weight (ZFW) calculations
The assumed weights vary around some kg / lbs. depending on the number of seats available on the aircraft.
a male passenger (incl. cabin luggage) weighs around 82kg (181 lbs.)
a female passenger around 67kg (148 lbs.)
a child around 50kg (110lbs.)
an infant 16kg (35 lbs.). These are statistical values but otherwise one would need to weigh every single passenger during check in to get his exact weight. Additional payload consists of baggage and cargo (such as mail or goods).

## Slide 15: maximum payload utilisation and Zero Fuel Weight (ZFW) calculations
Some of the problems caused by overloading an aircraft are:
The aircraft will need a higher takeoff speed, which results in a longer takeoff run.
Both the rate and angle of climb will be reduced.
The service ceiling will be lowered.
The cruising speed will be reduced.
The cruising range will be shortened.
Maneuverability will be decreased.
A longer landing roll will be required because the landing speed will be higher.
Excessive loads will be imposed on the structure, especially the landing gear

## Slide 16: Aircraft documentation
all log books, records, manuals and other data or documents described in Attachment 1 to the Acceptance Certificate,
all other log books, records (including, without limitation, records relating to the operation, service, inspection, maintenance, modification, testing, overhaul and repair of the Aircraft, the Engines and all Parts installed therein or thereon, including any FAA 8130-3 serviceability tags, or which are required to substantiate the airworthiness, age, use and or utility of the Aircraft, any Engine or any Part), manuals (including, without limitation, operating, maintenance, repair, overhaul or parts manuals), data, drawings, certificates, licenses, commitment letters received from the Airframe Manufacturer at delivery or other documents that are required to be maintained during the Lease Term under the terms of this Agreement, by the Aviation Authority, by the Approved Maintenance Program, or those that are otherwise provided to Lessee at Delivery or during the Lease Term with respect to the Aircraft or any Engine or any Part, and
all updates and additions to any of the foregoing and renewals, revisions and replacements thereof from time to time made in accordance with this Agreement or applicable law or otherwise.

## Slide 17: Aircraft documentation
Certificate of Airworthiness
The Certificate of Airworthiness (C of A) or Airworthiness Certificate is the formal document issued by the National Aviation Authority (NAA) to certify that an aircraft is airworthy. Every individual aircraft has to gain its own C of A which is achieved when it can be shown to conform to the certificated Type Design and is in a condition for safe operation. As a general rule civil aircraft are not allowed to fly unless they have a valid C of A.
Depending upon the regulatory regime, the C of A will need either periodic re-validation or periodic renewal which may involve the completion of a flight test schedule. In USA, this is explained in FAR Part 21 Subpart H - Airworthiness Certificates. In the EU, member states must use non-expiring C of A (EASA Form 25), as described in EASA Part 21 Subpart H. This non-expiring C of A is validated by issuing of Airworthiness Review Certificate (ARC), EASA Form 15a. The work to perform this review is carried out by the relevant CAMO working on behalf of the operator.

## Slide 18: Aircraft documentation
Characteristics:
Reference anniversary date on bottom left corner of certificate.
Kept valid by: a. Annual inspection on all aircraft. b. 100-hour inspection cycle on all Commercially registered aircraft. c. Compliance with all Airworthiness Directives (A/D’s). d. Insuring aircraft is operated within all limitations as specified by the operator’s manual.
Annual Airworthiness Information Report (AAIR) will be sent to owner 4 to 6 weeks prior to anniversary date on certificate. The owner is required to complete the form with the requested information and return to the appropriate body. This is for statistical purposes only. This form is not required to be carried in the aircraft.
The aircraft may be operated without a Certificate of Airworthiness for a test flight or ferry flight with the issue of a Temporary Flight Permit

## Slide 19: Aircraft documentation
Certificate of Registration
An aircraft shall not fly unless it bears the nationality and registration marks as required by the law of the country in which it is registered.

## Slide 20: Aircraft documentation
Characteristics:
Valid for the life of the aircraft unless sold, destroyed or taken out of service.
If the aircraft is sold, the seller completes the Transfer of Ownership card and forwards it to the transport authority immediately. The new owner completes the Application for Registration (reverse side of the Certificate of Registration) and forwards it to the transport authority for processing. An original bill of sale and a processing fee must accompany the form. The Interim Certificate of Registration is valid for a term of 90 days or until a new Certificate is received, whichever occurs first.
The owner must notify the transport authority within 7 days of a change of address.

## Slide 21: Aircraft documentation
Operator’s Handbook
An aeroplane flight manual (AFM) is a document produced by the aircraft manufacturer containing detailed information on the operation of the aircraft. The AFM details the recommended aircraft operating technique for normal, abnormal and emergency operation together with the Aircraft Performance that should be achieved when the aircraft is operated in accordance with these procedures.
The AFM is a vital part of the aircraft inventory and must be carried on all flights unless the National Airworthiness Authority (National Aviation Authority (NAA)) of the aircraft operator has formally accepted that the Operations Manual of the aircraft operator replicates all relevant AFM information for an aircraft. The AFM is specific to each aircraft and reflects the precise equipment and modification state of that aircraft. In practice, National Aviation Authority (NAA) dispensation not to carry the AFM on board an aircraft is commonly obtained by commercial aircraft operators.

## Slide 22: Aircraft documentation
Characteristics:
There must be a copy of the Pilot Operating Handbook or Aircraft Flight Manual as published by the Manufacturer in the aircraft; an Information Manual is not sufficient.
The Pilot Operating Handbook must be complete and include all amendments/supplements as issued by the manufacturer.
If the aircraft is not equipped with an Operating Handbook all limitations must be placarded conspicuously in the aircraft cockpit.

## Slide 23: Aircraft documentation
Aircraft Weight and Balance
Gravity is the downward force acting on all bodies vertically towards the centre of the Earth. The name given to the gravitational force is WEIGHT and for the principles of flight it is the total weight of the loaded aircraft. The magnitude of the weight force is determined by the aircraft’s mass. The greater the aircraft’s mass, the greater the weight force.
The weight force may be considered to act as a single force through the Centre of Gravity (CG). The CG is the point of balance and its position depends upon the mass and position of all the individual parts of the aircraft and the load that it is carrying. If the aircraft was suspended by a rope attached to its centre of gravity, the aircraft would balance.

## Slide 24: Aircraft documentation
The Balance point (Centre of Gravity - CG) is very important during flight because of its effect on the stability and performance of the aircraft. It must remain within carefully defined limits at all stages of flight.
The CG will move if the distribution of the load changes, e.g. by passengers moving about or by transferring fuel from one tank to another. The CG may move as the weight changes by fuel burning off or by parachutists leaping out. The all-up weight always decreases as the flight progresses.
The designers of an aircraft have determined the maximum weight / maximum take-off mass (MTOM) or weight (MTOW), based on the amount of lift the wings or rotors can provide under the operating conditions for which the aircraft is designed. The structural strength of the aircraft also limits the maximum weight the aircraft can safely carry. The ideal location of the center of gravity (CG) is very carefully determined by the designers, and the maximum deviation allowed from this specific location calculated.
A useful means of describing the load that the wings carry in straight and level flight (when the lift from the wings supports the weight of the aeroplane) is the Wing Loading factor, which is simply the weight supported per unit area of wing.

## Slide 25: Aircraft documentation
Characteristics:
Equipment List must be updated with any change. This will include a change in the Basic Empty Weight of the aircraft as well as a change in aircraft moment.
Each piece of equipment must be listed including its location (weight and arm).
The latest amendment shall be used for all weight and balance calculations.
In regards to aircraft reweighing: a. For aircraft less than 12,500 lbs, the aircraft must be reweighed at an AME’s discretion. b. For aircraft 12,500 lbs and greater, the aircraft must be reweighed every 5 years in addition to changes in the permanent equipment.

## Slide 26: Aircraft documentation
Insurance
Operators of aircraft are required by law to have certain minimum levels of insurance. The precise level depends on the Maximum Take-Off Mass (MTOM) of the aircraft and on the number of passengers carried.
Insurance must cover several separate areas.
Aircraft operators’ insurance must cover:
passengers
baggage
third party cover
cargo
risks of war and terrorism (‘war risk’)

## Slide 27: Aircraft documentation
On 30 April 2005, EC Regulation EC 785/2004 on insurance requirements for air carriers and aircraft operators came into force. The Regulation was subsequently amended on 6th April 2010. The Regulation, as amended, specifies the minimum levels of insurance required by aircraft operators and air carriers in respect of third party cover, passenger cover and cover for risks of war and terrorism.
In the United Kingdom the Civil Aviation Authority is the designated authority for monitoring compliance with the regulation on behalf of the Department for Transport.
The CAA will normally consider evidence of insurance, and therefore compliance with the Regulation, on the basis of the exchange rate between Sterling and the SDR in place at the inception of the policy. However, owners and operators need to be aware that it is their responsibility to ensure that adequate cover exists for each and every flight. If owners or operators have concerns over their level of cover they should contact their broker for advice.

## Slide 28: Aircraft documentation
Characteristics:
All privately registered aircraft must carry proof of minimum insurance.
All commercially registered aircraft must carry proof of minimum insurance

## Slide 29: Aircraft documentation
Logbook
Journey Log- There was once a huge controversy over what exactly constitutes a journey logbook. Everybody agreed you had to have one, but what is it? The original requirement was set out in 1944 without a precise definition. ICAO Annex 6 changed all that a few years ago, but we are still left with a decision on where the book should be kept.
The only document we have that comes even close to satisfying all the requirements are the Flight and Maintenance Log that are completed for every flight.
Article 34 in the 1944 ICAO Chicago Convention states that There shall be maintained in respect of every aircraft engaged in international navigation a journey log book in which shall be entered particulars of the aircraft, its crew and of each journey, in such form as may be prescribed from time to time pursuant to this Convention

## Slide 30: Aircraft documentation
Aeroplane nationality and registration.
Date.
Names of crew members.
Duty assignments of crew members.
Place of departure.
Place of arrival.
Time of departure.
Time of arrival.
Hours of flight.
Nature of flight (private, aerial work, scheduled or non-scheduled).
Incidents, observations, if any.
Signature of person in charge.
Characteristics:
The aeroplane journey log book should contain the following items and the corresponding roman numerals:

## Slide 31: Aircraft documentation
Characteristics:
Journey Logbook must be carried for every cross country flight. All flights must be recorded on a Flight Log Sheet where all applicable information such as weight, airtime, and flight time must be recorded. Flight Log Sheets shall be kept for a term of 2 years
The Journey Logbook shall be retained for a period of 3 years when full and the last two log entries shall be transferred into the new Journey Logbook
Every commercially registered aircraft shall be inspected every 50 hours of airtime. An extension of 10 hours may be permitted at the discretion of an AME, however the extension time must be removed off the following inspection (The next inspection would occur at 40 hours rather than 50 hours).
All inspections must be recorded in the Journey Logbook stating the work completed and the time of next inspection due. The AME conducting the work shall sign the Logbook. In the case of major work conducted on a critical flight controls such as power plant or flight controls, a second signature of an AME inspecting the work or Pilot conducting a flight test shall be required

## Slide 32: Aircraft documentation
Logbook
Journey Log- There was once a huge controversy over what exactly constitutes a journey logbook. Everybody agreed you had to have one, but what is it? The original requirement was set out in 1944 without a precise definition. ICAO Annex 6 changed all that a few years ago, but we are still left with a decision on where the book should be kept.
The only document we have that comes even close to satisfying all the requirements are the Flight and Maintenance Log that are completed for every flight.
Article 34 in the 1944 ICAO Chicago Convention states that There shall be maintained in respect of every aircraft engaged in international navigation a journey log book in which shall be entered particulars of the aircraft, its crew and of each journey, in such form as may be prescribed from time to time pursuant to this Convention